## Slide 1
Training Course contents
IDB
  Different types of IDB
  IDB Creation
  Different Template
  Connection
  Remote Testing
  VSWR
  BB Backup Time
  Alarm Logs
  Alarms Checking
  Sync Source
  KPI troubleshooting
  Sector Swap
  SFP

## Slide 2
IDB
  Different types of IDB
  IDB Creation
  Different Template
IDB

## Slide 3
IDB
OMT Information and 2G commissioning
Connect DUG by OMT
Format Flash card and load IDB and software

## Slide 4
IDB
Create IDB
After load Flash card , create IDB from configuration > create IDB

## Slide 5
Make IDB as required sectors and load in DUG
IDB

## Slide 6
Load IDB and SW by OMT software as below have mentioned
IDB

## Slide 7
Select RBS type
Select RBS type
IDB
Notes: نمایش منوی Create IDB

## Slide 8
Select subrack options
Select climate system
IDB
Notes: پاور را انتخاب می کنیم

## Slide 9
After finish press OK
Select Antenna sector setup
IDB
Notes: بر روی ok کلیک می کنیم

## Slide 10
Select transmission option STN or SIU
Select sectors option
IDB
Notes: نوع STN را انتخاب می کنیم

## Slide 11
Select RUS type
IDB

## Slide 12
Select TRX as per plan e.g. 900 2+2+2
IDB

## Slide 13
Recheck configuration here then press OK
IDB
Notes: بر روی ok کلیک می کنیم

## Slide 14
Right click at GSM > Define > Node Parameters
Select MCTR as per plan
IDB

## Slide 15
Select Node B1 for Master DUG
Add Nodes for WCDMA, 1800 , LTE
IDB

## Slide 16
Here Node will show
Present all required RU and units
IDB

## Slide 17
Define RU as per HW structure
Select RU position
IDB

## Slide 18
After RU definitions
Define Smoke : Right click Alarms > Define > Alarm Inlets
IDB

## Slide 19
Select Smoke Alarm
Press Apply
IDB
Notes: بر طبق شکل آلارم Smoke را تعریف می کنیم

## Slide 20
Right click Transmission > Define > Transmission
Select here type of Transmission
IDB

## Slide 21
Connection
  DUG to DUG connection
  DUG to DUW Connection
  DUG to DUS connection
Connection

## Slide 22
RBS TCU Connection
RBS and DUG connection should be done between ET ports. The ETA port in the first DUG should be connected to ETA port on the TCU. And the ETA port in the second DUG should be connected to ETA port on the TCU. Each ET ports support 2E1s.
If 4E1 used per DUG then, The ETA port in the first DUG is to be connected to ETA on TCU, ETB port in the first DUG is to be connected to ETB on TCU. And the ETA port in the second DUG is to be connected to ETC on TCU; ETB port in the second DUG is to be connected to ETD on TCU.
The Connection towards TN has to be done via TN_A port with a straight (RJ45) cable.
Connection

## Slide 23
  Remote Testing
  VSWR
  BB Backup Time
  Alarm Logs
  Remote Testing

## Slide 24
Check Faults from Radio part that which RUS has VSWR issue
  Remote Testing ( VSWR )

## Slide 25
  Remote Testing ( BB Test )

## Slide 26
For taking RBS logs please follow below steps
  Remote Testing ( RBS Logs )

## Slide 27
Check Alarm details in Description and than take necessary actions written in ACTION part
  Alarm Checking

## Slide 28
  Sync Source
  Sync Source

## Slide 29
  Sync Source

## Slide 30
  Troubleshooting
a. Check physical links to the transport network are up.
b. If using Ethernet transport, verify that Ethernet Port TN_A is enabled, TN_A LED should be blinking
c. If using E1 transport, verify that all E1 ports are enabled. If there are 2 E1s connected, the leds on E1/T1 Port ETA should be on
Note: The Ethernet ports towards the TN will not be enabled until after the RBS is integrated.
d. Check alarms
"getalarmlist"
Note: The TCU should be fault free.
e. ping PGW IP address in configuration file to verify that BSC is reachable
"ping "PGW IP Address""
  KPI troubleshooting

## Slide 31
Complete Swap
Partial Swap
CPRI Swap
  Sector Swap

## Slide 32
Complete Sector Swap
  For this kind of Swap means that one sector is completely swapped with another sector for example XA is fully swapped with XB, both TX and RX branch
  Partial Swap
    Partial Swap means that TX and RX cable has been swapped on same sectors.
  CPRI Swapped
    For checking this kind of swap please verify that CPRI cables between DUG/DUW/DUS and RUS should be connected on correct port of DUG/DUW/DUS.
  Sector Swap

## Slide 33
During troubleshooting sector fluctuation or sector down please verify that CPRI installed in DUW/DUS and RRUs are of same product.
  SFP